## Slide 1
Flexible Allocation & Attribution
RSB and ISCC Methodology Review
What the standards actually permit, under what conditions, and why
Every claim on the pages that follow carries a verbatim quote, with source title, version, section, and page.

## Slide 2
1
The question, framed neutrally
Under what conditions does a recognized fuel-certification scheme allow non-proportional (“flexible”) allocation of a sustainability claim — as opposed to strict energy- or mass-proportional allocation?
Three standards were checked directly:
• RSB Standard for Advanced Fuels (RSB-STD-01-010, v2.8, April 2026)
• RSB Standard for ICAO CORSIA (RSB-STD-12-001, v1.7, April 2026) — a separate RSB standard, not a variant of the one above
• ISCC Questions and Answers on the Certification of Co-Processing (v1.0, valid from 22 September 2025)
Two terms are kept strictly separate throughout, because the standards themselves separate them:
Allocation — how GHG emissions are divided among co-products
Attribution — how a sustainability claim (“this output is X% biogenic”) is assigned to a specific output
Scope: RSB Advanced Fuels, RSB ICAO CORSIA, and ISCC's co-processing guidance. Not checked: EU RED, LCFS, or other schemes.

## Slide 3
2
Allocation vs. attribution — in the standards' own words
ALLOCATION
(the GHG emissions math)
“Allocation of the GHG emissions among the outputs shall be performed on an energy basis.”
— RSB Standard for Advanced Fuels, RSB-STD-01-010 v2.8, Annex IV, Note 7, p.28
This rule does not change even when the sustainability claim is allocated flexibly (see next slides). The emissions math and the claim are two separate things.
ATTRIBUTION
(the sustainability claim)
“...attribute the bio-based portions of the input(s) or feedstock(s) to specific product(s) or output(s) using flexible attribution...”
— RSB Standard for Advanced Fuels, RSB-STD-01-010 v2.8, §2.4.2(c), p.11
This is the mechanism that lets one output carry a 100% claim while another carries 0%, subject to guardrails covered on the next slides.
RSB-STD-01-010 v2.8, §2.4.2 and Annex IV, Note 7 (p.11, p.28).

## Slide 4
3
RSB is not one scheme
“RSB” covers multiple distinct standards. The one that allows flexible attribution and the one used for CORSIA-eligible SAF are different documents — and they disagree on this point.
RSB Standard for Advanced Fuels
RSB-STD-01-010, v2.8, April 2026
Flexible attribution allowed as one of three options for documenting biogenic/fossil fractions:
mass balance, radiocarbon method, or flexible attribution.
§2.4.2, p.11
RSB Standard for ICAO CORSIA
RSB-STD-12-001, v1.7, April 2026
No flexible option. Co-product allocation is mandatory and energy-basis only:
“...energy-based allocation shall be used to assign emission burdens to all co-products...”
§3.4.7.1, p.23
STD-01-010 v2.8 from rsb.org; STD-12-001 v1.7 from rsb.org's current library listing.

## Slide 5
4
RSB Advanced Fuels: the mechanism and its cap
Worked example from the standard itself (Annex IV, p.29):
“1.1t of jet fuel will be sold with 100% bioattributed claim, while the remaining quantity of products will be sold with 0% bioattributed claim. Note that the amount of jet fuel sold with 100% flexible attributed claim is limited by the amount of biogenic carbon content in the biobased feedstock considering the efficiency in converting the feedstock into output.”
The physical cap: Annex IV Step 1 (p.26) — eligible carbon exiting the process = feedstock mass × carbon content × conversion efficiency. Worked figure: 10t of biogenic carbon entering at 90% conversion efficiency yields 9t of eligible carbon — the ceiling on how much output can carry the claim, regardless of which output it's assigned to.
Guardrails, each from the standard's own text:
• GHG emissions still allocated energy-basis: “Allocation of the GHG emissions among the outputs shall be performed on an energy basis.” (Annex IV, Note 7, p.28)
• Balance discipline: non-negative balance required every 3 months (§2.4.5, p.12)
• Boundary limits: one site, connected sites, or sites where double-booking is contractually prevented (§2.4.5, p.12)
• Claim-label limit: “Claims may not refer to a physical sustainable content of the output product” — alternative labels like “RSB-Compliant Advanced Fuel” must be used instead (§2.5.4, p.12)
RSB-STD-01-010 v2.8, §2.4.5, §2.5.4, Annex IV, pp.12, 26, 28, 29.

## Slide 6
5
RSB-CORSIA: why the flexible option isn't available
The mandatory rule (RSB-STD-12-001 v1.7, §3.4.7.1, p.23):
“Whenever a processing step along the SAF supply chain results in the co-production of multiple commodities..., energy-based allocation shall be used to assign emission burdens to all co-products in proportion to their contribution to the total energy content... of products and co-products.”
This standard also incorporates RSB Advanced Fuels by reference for wastes, residues and by-products (§1.5, p.10) — the same standard that offers flexible attribution. So why doesn't that option carry over?
Its own precedence clause answers that (§D, p.6):
“In the event of inconsistency between this RSB standard and the RSB Principles & Criteria [RSB-STD-01-001] or other RSB standards and procedures, this standard shall prevail.”
Mandatory energy-based allocation (§3.4.7.1) is this standard's own rule — so it overrides the flexible option that RSB Advanced Fuels would otherwise offer.
RSB-STD-12-001 v1.7, §1.5, §3.4.7.1, §D, pp.6, 10, 23. Version 1.7 published 7 April 2026; effective immediately per §C, p.6.

## Slide 7
6
ISCC: a two-stage rule, and a provisional one
ISCC's Co-Processing Q&A (v1.0, valid from 22 Sept 2025) addresses this directly, p.21:
“At the processing unit a proportional assignment is required to comply with co-processing rules. When further trading the co-processed fuel, a flexible assignment shall be allowed until further notice from the EC and an updated Implementing Regulation 2022/996.”
Same page, ISCC's own characterization of the state of play:
“The topic of proportional or flexible assignment is still under discussion. Certain Member States (MS) are in favour of flexible allocation of sustainable attributes to a specific portion of the fuel, while others prefer proportional allocation until certain element of the supply chain... As the ISCC mass balance guidance document is still awaiting approval from EC, flexible allocation of sustainability attributes shall be allowed until further notice.”
Reading: proportional assignment is mandatory at the point of processing itself; flexible assignment is permitted only further downstream in trading, and only as a stopgap while the EU has not yet finalized its position — not a settled, published methodology the way RSB Advanced Fuels' Annex IV is.
ISCC Q&A on Co-Processing v1.0, p.21, dated 22 Sept 2025. Whether the EC has since finalized the referenced revision to Implementing Regulation 2022/996 is not confirmed.

## Slide 8
7
Guardrails, side by side
Guardrail | RSB Advanced Fuels | ISCC (co-processing)
Physical cap on the claim | Yes — capped by feedstock carbon content × conversion efficiency (Annex IV, p.26) | Yes — proportional assignment mandatory at the processing unit itself (p.21)
GHG emissions allocation | Still energy-basis, regardless of the claim (Annex IV, Note 7, p.28) | Not addressed separately from bio-content in the ISCC Q&A
Claim-label restriction | Yes — no “physical sustainable content” claim; alternate labels required (§2.5.4, p.12) | Not addressed in the ISCC Q&A
Balance / bookkeeping | Non-negative balance every 3 months, documented (§2.4.5, p.12) | General ISCC mass-balancing rules apply once bio-content is established (p.21)
Status of the mechanism | Published, worked methodology with numeric examples (Annex IV–V) | Provisional — “shall be allowed until further notice from the EC” (p.21)
Cell contents summarize citations detailed on slides 5–7; see the citation appendix for exact quotes.

## Slide 9
8
The answer, in one table
 | RSB-CORSIA | RSB Advanced Fuels | ISCC (co-processing)
Flexible allocation/attribution allowed? | No | Yes | Yes — downstream of the processing unit only
Governing citation | RSB-STD-12-001 v1.7, §3.4.7.1, p.23 | RSB-STD-01-010 v2.8, §2.4.2/2.4.5/Annex IV | ISCC Co-Processing Q&A v1.0, p.21
Nature of the rule | Mandatory energy-basis allocation | Published, capped, worked methodology | Provisional stopgap pending EU regulation
Every one of these standards treats “flexible” differently. Only RSB Advanced Fuels offers it as a mature, published methodology with a numeric cap. RSB-CORSIA doesn't offer it at all. ISCC's version is provisional and explicitly contested among EU Member States.
See slides 4–7 for full quotes and the citation appendix for the complete source list.

## Slide 10
Appendix A
Sources
RSB Standard for Advanced Fuels, RSB-STD-01-010, Version 2.8, published April 2026, Status: Final Draft.
Cited: §2.4.2 (p.11), §2.4.3 (p.11), §2.4.5 (p.12), §2.5.4 (p.12), Annex IV (pp.26, 28, 29), Annex V (pp.30–32).
Local file: rsb-std-01-010-v2.8.pdf.
RSB Standard for ICAO CORSIA, RSB-STD-12-001, Version 1.7, published April 2026, Status: Final.
Cited: §D (p.6), §1.5 (p.10), §3.4.5 (p.20), §3.4.7.1–3.4.7.2 (p.23).
Source: rsb.org/wp-content/uploads/2026/04/RSB-STD-12-001-RSB-ICAO-CORSIA-ver-1.7.pdf, linked from rsb.org's current library listing for STD-12-001.
ISCC, Questions and Answers on the Certification of Co-Processing, Version 1.0, valid from 22 September 2025.
Cited: “Sustainability requirements” (p.21), “Co-processing GHG methodology” (p.19), system boundary discussion (p.7).
Local file: “ISCC Co-Processing QA v1.0 Sept 2025.pdf”.
Not checked in this review: EU RED, LCFS, or any ISCC source other than the Co-Processing Q&A above.

## Slide 11
Backup
Numeric detail held in reserve for follow-up questions

## Slide 12
Backup 1
RSB Annex IV — the physical cap, in numbers
From the standard's own Figure 1 (Annex IV, p.29):
• Inputs: 21t biomass feedstock (10t biogenic carbon) + 98t fossil feedstock (68.6t fossil carbon)
• Process conversion efficiency: 90%
• Outputs: 1.1t SAF (carrying 0.9t of the attributed biogenic carbon), 2.4t fossil-based jet fuel (2.1t fossil carbon attributed), plus other fossil-based products (59.7t fossil carbon attributed)
• Resulting carbon footprint: 0.98 tCO2eq/t SAF vs. 1.69 tCO2eq/t fossil jet fuel
Note in the figure: “the input of biogenic carbon is 1t. The output of biogenic carbon attributed to the final product is 0.9t since a conversion efficiency of 90% was considered.”
The cap is mechanical, not a matter of operator discretion: the standard's equation [1] (p.26) fixes the maximum eligible carbon before any attribution choice is made.
RSB-STD-01-010 v2.8, Annex IV, Figure 1 and accompanying text, p.26 and p.29.

## Slide 13
Backup 2
RSB Annex V — flexible attribution of process inputs
Annex V (added in v2.8, p.30) extends flexible attribution beyond the biogenic feedstock itself to process inputs and utilities (electricity, steam, oxygen) in a co-processing SAF example.
Worked comparison (p.32):
• Without flexible attribution of inputs: SAF GHG intensity = 68 g CO2e/MJ
• With flexible attribution of inputs: SAF GHG intensity = 30.25 g CO2e/MJ
Guardrail governing this (Step 3, p.32): “You may not attribute more of an input than the amount... used in the co-process.” Low-carbon inputs are attributed first, up to their actual available quantity, before higher-carbon inputs are used to cover the remainder — the same cap logic as Annex IV, applied to utilities rather than feedstock carbon.
RSB-STD-01-010 v2.8, Annex V, pp.30–32.

## Slide 14
Backup 3
ISCC — the co-processing Q&A in fuller context
What determines bio-content per output, before any allocation question arises (§2–4, pp.6–15): direct ¹⁴C radiocarbon testing at the co-processing system boundary, or an indirect method (mass balance / energy balance / yield) validated against ¹⁴C. This is a measurement question, not a discretionary attribution.
Once measured, GHG intensity: “As a general rule, in accordance with point 1 of the GHG methodology, all (fuel) types shall be considered to have the same emission intensity. The overall emissions... should thus be divided by the energy in the overall produced fuels.” (p.18, quoting the RFNBO and RCF guidance, Q46)
Regulatory anchor named in the source itself: “This document is a compilation of clarification on queries regarding the certification of co-processed fuels per the COMMISSION DELEGATED REGULATION (EU) 2023/1640...” (p.4)
Backdrop for the p.21 finding on the summary slides: bio-content itself is measured and energy-allocated by default; the open question is specifically whether the resulting claim can later move flexibly between fuel batches once traded — and that piece is what ISCC calls provisional.
ISCC Questions and Answers on the Certification of Co-Processing, v1.0, pp.4, 6–15, 18, 21.