## Slide 1
BASCO SYNC · POST-MORTEM
D-Series TCLP
What went wrong, and how we stop it happening again

## Slide 2
WE HAVE BEEN HERE BEFORE
2024: 236 t verified, none credited
• The Vaulted permit required salting the oil's water fraction "to a minimum concentration of 190,000 mg/L before injection."
• Injection ops chose not to measure chloride. They calculated the salt dose from oil volume and water content: "conductivity (not measured due to oily interference)."
• The calculation assumed the oil in the tank was the oil that went down the hole. Phase separation and leftover oil broke that, and four May batches came in under the limit.
• The verifier asked: "Where are conductivity tests of injectate documented?" There were none.
• Result: the May 2024 verification failed. 236.23 t verified, "not eligible for crediting."
Notes: Sources: Vaulted KDHE authorization as quoted in our Dec 2024 technical memo; ops note, Aug 2024 (#injection-ops-ks); 350Solutions unsuccessful verification report, Jan 21, 2025 (batches 200006, 200008, 200011, 200013).

## Slide 3
2026
D-Series TCLP: the same pattern
Unclear result
Results ranged from passing (lower pyrolysis temperature) to cresols at 855 mg/L against a 200 limit. One pyridine result was "ND" at a reporting limit above the 5.0 limit.
No rule on which result
No agreed policy on which result sets the blend limit or why. The limit was set on one result, then doubled on a lower one.
No cross-team sign-off
The blending plan went into use without review or sign-off from the other teams that hold part of the picture.
No proof it works
No testing of actual blends and no record tying each blend to the result behind it. The verifier has now asked exactly this (ISS-130).
Notes: Passing results: two earlier D-Series oils at ~475 °C. Failing: July sample cresols 855 mg/L (revised report; 877 also cited); August sample cresols 530, pyridine 7.52. July report also notes analysis outside holding time and accreditation not specified. Blend limit: ~9 totes on the first result, ~18 totes from 8 Sep on the August result.

## Slide 4
WHY IT HAPPENED
Each team held part of the picture
Lab
Test results, and what they can and can't show.
Engineering
Operating conditions that change the results.
Injection ops
The blend plan and what actually went in.
EHS / regulatory
Permit terms and the hazardous-waste call.
MRV
What the verifier needs to see.
There was no point where these came together before oil went into the well.

## Slide 5
THE COMMON THREAD
No one is clearly holding this
Both times, a method went into use without:
• an agreed standard for proving it works
• review across the teams that hold the pieces
• a clear owner for showing the site meets its permit
That gap is what we need to close, now.

## Slide 6
A STARTING POINT FOR DISCUSSION
Suggested: who could hold what
Team | Could hold
Operations | Running the site so permit compliance can be shown to a third party. Owns the method and its records.
Engineering | The tools and process conditions operations needs to do that.
Lab | Test design, results, and what each result can and can't support.
EHS / regulatory | Reading the permit and hazardous-waste rules; confirming a method meets them.
MRV | Defining the evidence the verifier needs and presenting it.
A proposal to react to, not a decision.

## Slide 7
GOING FORWARD
What we need to decide
• Who owns showing that what goes down the well meets the permit.
• What review and sign-off a new oil, blend or treatment needs before first injection.
• A rule for which test results count, and how every result reaches the teams that need it.
• For D-Series now: a testing plan, a record for each blend, and an answer to the verifier on ISS-130.