## Slide 1
SAF Credit Generation
Pathway Analysis and Recommendation
Charm Industrial | Internal | June 2, 2026

## Slide 2
The Opportunity
Charm's bio-oil qualifies as a SAF feedstock at an FCC refinery, creating an opportunity to generate SAF credits alongside CDR credits from the same production process.
What we have
Bio-oil with Isometric-validated Cradle-to-Gate CI and established upstream methodology
What we want
SAF credits for bio-oil used as refinery feedstock, with free biogenic allocation to SAF output
The question
Which accounting pathway within the SFC MBM framework is viable for Charm?
SFC MBM (SFC-SPEC-001) is the governing framework and 123 Carbon is the registry. SFC MBM names two certified pathways (ISCC, RSB) and includes a non-certified methodology track with specific criteria. All three were evaluated.

## Slide 3
The Framework: SFC MBM + 123 Carbon
SFC-SPEC-001 (SFC MBM) is the standard under which SAF credits will be generated and registered. 123 Carbon is the registry. All viable credit pathways operate within this framework.
Three pathways exist within SFC MBM:
Named: ISCC Certification
ISCC certification satisfies SFC MBM requirements and guarantees 123C acceptance. Practical friction at Steps 4, 1, and 6 makes this operationally difficult.
High friction
Named: RSB Certification
RSB certification satisfies SFC MBM requirements and guarantees 123C acceptance. GHG savings threshold fails at current bio-oil CI.
Fails GHG threshold
Non-Certified Methodology
SFC MBM includes a provision for non-certified methodologies meeting specific criteria. Criteria must first be clarified by 123C / SFC before methodology development can begin.
Recommended
Full SCE (no framework, Charm manages registry internally) is evaluated separately as the least desirable alternative.

## Slide 4
The 14-Step Production System
1
Biomass sourcing and collection
2
Biomass transport to conversion site
3
Biomass conversion (pyrolysis)
4
Allocation of tree-to-gate emissions to co-products
5
Transport of bio-oil to refinery
6
Refinery co-processing into fuel co-products
7
Allocation of marginal refinery emissions to co-products
8
Allocation of biogenic carbon credit to fuel co-products
9
Transport of fuel(s) to blend point
10
Quantification of tree-to-wheel CI
11
Quantification of GHG reductions vs. fossil fuel baseline
12
Verification of quantified reductions
13
Credit issuance on a registry
14
Credit delivery, retirement, and integrity
Steps 1-5 and 9: Isometric-validated, reused. Steps 6-8: Novel development. Steps 10-14: CI calc, stakeholder validation, 123C registry.

## Slide 5
CORSIA: Ruled Out Before the Framework Question
CORSIA was evaluated as a potential pathway before settling on SFC MBM. It is ruled out regardless of framework because of a structural disqualifier.
Step 8 — Disqualifying: Free allocation of biogenic carbon to SAF output is prohibited
CORSIA requires that the bio-based proportion of each refinery output is fixed by the process conversion factor. The operator cannot designate which output receives the biogenic credit. This makes the SAF credit economics unworkable. This is a structural constraint, not a compliance gap. There is no workaround within CORSIA.
CORSIA and all CORSIA-adjacent schemes are excluded from further consideration.
Color code: Red = Disqualifying Yellow = Friction Green = Validated / Recommended

## Slide 6
RSB + 123C: Named in SFC MBM — But Fails the GHG Threshold
RSB certification is named in SFC MBM, which would guarantee 123C acceptance. But the GHG savings threshold is a disqualifying issue at Step 11, and two additional friction points compound the problem.
Step 11
GHG savings threshold — Disqualifying
RSB Principle 3b requires >=65% savings vs. 90 gCO2e/MJ fossil comparator (<=31.5 gCO2e/MJ). Transitional pathway to 2035: >=50% savings (<=45.0 gCO2e/MJ). Charm WODO CI 2025: 0.8 tCO2e/t bio-oil = 45.3 gCO2e/MJ upstream assuming SAF LHV of 43,200 MJ/t. 0.3 gCO2e/MJ above the transitional threshold before refinery marginal emissions or downstream transport.
Step 4
Economic allocation — Compounding
RSB mandates economic allocation. Bio-oil commands a much higher market price than biochar, so economic allocation likely assigns MORE emissions to bio-oil — making the Step 11 problem worse, not better.
Step 1
Supply chain certification burden — Friction
RSB (or FSC — to be confirmed) certification required for every biomass First Gathering Point. RSB guidance may allow FSC as an alternative, as ISCC does; this should be clarified against the RSB standard before assuming full RSB certification is required throughout.
Color code: Red = Disqualifying Yellow = Friction Green = Validated / Recommended

## Slide 7
ISCC + 123C: Named in SFC MBM — But Significant Friction at Multiple Steps
ISCC certification is named in SFC MBM, which would guarantee 123C acceptance. But three steps in the system chain create meaningful friction.
Step 4
Allocation conflict
ISCC PLUS V3.4.2 states energy allocation should always be used when the main product is used energetically. Charm uses carbon-mass-balance (a form of mass allocation). Auditor challenge risk at certification.
Step 1
Supply chain certification burden
Every First Gathering Point must be ISCC certified (or upstream forest must be FSC Forest Management certified). Charm wildfire-reduction whole logs likely classify as forestry primary product, triggering the full Level A risk assessment and certification chain. How Isometric's independent forester carve-out maps to ISCC requirements is not established.
Step 6
Refinery certification
The FCC refinery must also be ISCC certified. Charm does not control this.
Note: ISCC PLUS has no minimum GHG savings threshold (quantification is voluntary). Favorable for CI, but ISCC PLUS functions primarily as a sustainability certification, not a GHG methodology.
Color code: Red = Disqualifying Yellow = Friction Green = Validated / Recommended

## Slide 8
Recommended: Non-Certified Methodology Track Under SFC MBM
SFC MBM includes a provision for non-certified methodologies meeting specific criteria. This is the recommended path. The four stages must run in order — each one defines the scope of the next.
1
Clarify non-certified criteria (123C / SFC)
123C and/or SFC clarifies what criteria a non-certified methodology must meet to qualify under SFC MBM. Currently unknown. This is the prerequisite for all other work — criteria become part of the scope of work put to the methodology partner.
2
Define customer requirements
Key buyers specify non-quantification requirements: community benefit standards, audit preferences, traceability criteria. Combined with SFC MBM criteria, these define the full scope the methodology must satisfy.
3
Select third-party methodology partner
Key customers identify a preferred methodology developer (e.g., Carbon Direct, EcoEngineers). Customer identification ensures developer credibility and builds acceptance in from the start.
4
Develop, validate, and register
Develop methodology satisfying SFC MBM criteria + customer requirements + Charm/refinery operability. All stakeholders validate (123C, customers, Charm, refinery) before launch. 123 Carbon issues and manages credits.

## Slide 9
Recommended Path: System Approach by Step
1-5
Isometric-validated methodology reused: biomass eligibility, tree-to-gate CI, co-product allocation, transport. Will be incorporated into the overall methodology framework with the third-party partner.
Isometric-validated; third-party incorporation
6-8
Novel methodology developed with third-party partner: refinery co-processing, marginal emissions allocation, free allocation of biogenic carbon to SAF. Must satisfy SFC MBM non-cert criteria + customer requirements.
Third-party partner + stakeholder validation
9
Transport emissions to blend point. Isometric-validated methodology reused. Will be incorporated into the overall methodology framework with the third-party partner.
Isometric-validated; third-party incorporation
10-11
CI calculation + fossil fuel comparator selection. Bounded novel work; subject to same third-party development and all-stakeholder validation as Steps 6-8.
Third-party partner + stakeholder validation
12
Validation by 123C, customers, Charm, and refinery before launch. Verification scope and frequency to be determined.
All stakeholders
13-14
Credit issuance, management, retirement, double-counting prevention.
123 Carbon

## Slide 10
The Alternative: Full Self-Certification (SCE)
If Charm does not pursue the SFC MBM framework, the remaining option is full SCE: Charm internally develops the methodology and manages the registry, outside of SFC MBM and without 123 Carbon.
Pros
Cons
Lowest operational lift of any option
Quickest to execute
Plays well with existing CDR MRV
Upstream methodology is already Isometric-validated
No external checks on Charm calculations — straightforward target for conflict-of-interest challenges
No registry-level double-counting protection
Not tied to SFC MBM — credit acceptance by buyers in that framework is uncertain
Weakest market integrity signal
Least likely to satisfy customer requirements
Assessment: Viable mechanically, but least likely to hold up under customer or market scrutiny.

## Slide 11
System-Level Risks
No precedent: dual CDR + SAF accounting on the same process
The prevailing assumption in the field is that CDR credits and biofuel CI credits on the same process are mutually exclusive. Charm's co-product structure may allow both — biochar CDR credits on the solid, bio-oil SAF credits on the liquid — but this requires affirmative methodology development. No existing framework addresses it.
Co-product substitution uncertainty
In CDR accounting, biochar co-product substitution is credited against bio-oil CI. Whether this carries over to the biofuel CI context is not established. If it cannot be applied, the bio-oil CI rises.
Customer requirement conflict
Different key customers may have incompatible requirements: different preferred methodology developers, different community benefit standards, different audit requirements. Charm must establish internal alignment on customer prioritization before outreach begins — this cannot be resolved reactively.
Methodology acceptance risk
A non-certified methodology has no pre-established market credibility. Stakeholder validation (123C, customers, Charm, refinery) reduces but does not eliminate the risk of a challenge after launch.

## Slide 12
Next Steps
1
Clarify SFC MBM non-certified criteria (123C / SFC)
This is the prerequisite for all downstream work — criteria define the scope of work put to the methodology partner. In parallel: Jeroen to report back on ISO 14083 interaction, methodology developer accreditation requirements, and Isometric role in biofuel CI certification.
2
Internal alignment on customer conflict prioritization
Establish which customer relationships take priority if buyer requirements diverge. Must be resolved before customer outreach.
3
Customer outreach: define requirements, identify partner
Work with Amazon, DHL, and other key buyers to specify non-quantification requirements and identify a preferred third-party methodology developer.
4
Develop and validate methodology
Work with selected partner to develop methodology satisfying SFC MBM criteria, customer requirements, and Charm/refinery operability. All-stakeholder validation before launch.