## Slide 1
SAF Methodology Framework
Bio-Oil → FCC Co-Processing → SAF Credit | Charm Industrial
ISCC-downstream variant — ISCC PLUS conventions replace RSB for Steps 7–9, 11–12
Steps 1–6, 10: Charm CDR methodology (validated PDD v1.12) · Steps 7–9, 11–12: Bolt-On (ISCC PLUS) · Steps 13–15: 123Carbon (SFC MBM)

## Slide 2
Design Principles — “one root, many branches”
One production system serves both carbon removal (CDR) and environmental attributes (EACs) — one architecture from the most applicable parts of each.
1 Unusual dual mandate — one pyrolysis system generates intermediate products feeding both CDR and EACs. No single end-to-end methodology fits both.
2 Both-and, not either-or — the architecture must accommodate multiple crediting schemes without undue burden or loss of accounting integrity.
3 One root, many branches — different pieces may use different methodologies, bundled/unbundled as needed.
4 Leverage the CDR investment — reuse Charm’s validated Isometric CDR work for EACs.
“Bolt-on” concept: the root (biomass qualification + pyrolysis CI) stays on Charm’s validated CDR methodology; reputable published methodologies bolt on downstream. This variant uses ISCC PLUS as the co-processing branch — chosen because ~5–6 US refineries are ISCC-certified for co-processing vs 0 under RSB.

## Slide 3
STEP 1 OF 15 · Biomass Qualification
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, §B — Project Eligibility
• Underlying: Biomass Feedstock Accounting v1.3 — Sustainability Criteria SC1–SC7 (§2.1), Prohibited Feedstocks (§4.1), Market Leakage (§4)
WHAT IT IS
• Three source-agnostic eligibility gates from BFA v1.3; Counterfactual Storage (§3) is the one gate excluded — a removals concept with no role in a fuel-displacement claim.
WHY IT’S BEING USED
• Charm’s CDR project already cleared these gates under the PDD; the SAF claim reuses the determination. Module is tailored to woody biomass from wildfire fuels reduction.

## Slide 4
STEP 2 OF 15 · Biomass Sourcing & Collection
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, §B — Monitoring Plan
• Underlying: BFA v1.3 §2.1 + Appendix 1 (origin, harvest authorization, mass per batch)
WHAT IT IS
• Monitoring-plan framework records feedstock origin, authorization and mass per supply-chain batch. Wildfire fuel-reduction biomass qualifies as waste/residue → zero emissions up to collection.
WHY IT’S BEING USED
• Framework already in place for the CDR project; reusable for SAF with no new sourcing documentation.

## Slide 5
STEP 3 OF 15 · Biomass Transport to Conversion Site
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, §B — Project Boundary & Monitoring Plan
• Underlying: Transportation Emissions Accounting v1.1 §3.3 (Distance-Based: CO₂e = D × W × EF); §3.4 + App.1 (EF currency floors)
WHAT IT IS
• PDD sets the boundary/monitoring for truck & rail legs; the Transportation module gives the distance-based calculation. EFs updated ≥ annually per the PDD.
WHY IT’S BEING USED
• Already inside Charm’s validated PDD boundary; transfers to the SAF claim unchanged. Covers multimodal (rail + truck).

## Slide 6
STEP 4 OF 15 · Biomass Conversion (Pyrolysis)
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, §B — Technical Description
• Underlying: Bio-oil Geological Storage v1.2 §4/§8.1 (Production Batch), §8.5.6 (tailgas CH₄ × GWP), Energy Use Accounting v1.3 (facility energy)
WHAT IT IS
• Pyrolysis converts biomass to bio-oil (the SAF feedstock). Direct emissions = tailgas CH₄ (CO₂ not discounted — feedstock would decay < 15 yr). Facility energy via Energy Use module.
WHY IT’S BEING USED
• Charm’s existing validated conversion methodology — no new development. Note: capex embodied emissions currently in production CI; moving to amortize against gross removals, aligning with ISCC (EU 205 excludes machinery/equipment manufacture).

## Slide 7
STEP 5 OF 15 · Allocation of Tree-to-Gate Emissions to Co-Products
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, Appendix 6 — GHG Statement Methodology
• Underlying: GHG Accounting Module v1.1 §6.1; Bio-oil Geological Storage v1.2 §8.5.5.1
WHAT IT IS
• Charm allocates tree-to-gate process emissions across co-products (biochar / bio-oil fractions) on a CARBON-MASS basis (the protocol’s optional energy method is not used at this step).
WHY IT’S BEING USED
• Keeps SAF co-product accounting identical to the validated CDR treatment on the same pyrolysis process. NOTE: ISCC downstream (Step 8) allocates by energy — the basis switches mid-chain and must be documented.

## Slide 8
STEP 6 OF 15 · Bio-Oil Transport to Refinery
Charm CDR Methodology
NORMATIVE REFERENCE
• Charm PDD v1.12, §B — Project Boundary & Monitoring Plan
• Underlying: Transportation Emissions Accounting v1.1 §3.3 (rail + truck)
WHAT IT IS
• Bio-oil shipment to the FCC refinery uses the same validated transport-accounting method (distance × mass × mode EF); only the destination is SAF-specific.
WHY IT’S BEING USED
• Method already validated in the CDR PDD; carries over without new methodology and keeps verifier review consistent.

## Slide 9
STEP 7 OF 15 · Refinery Co-Processing into Fuel Co-Products
Bolt-On — ISCC PLUS
NORMATIVE REFERENCE
• ISCC PLUS 203-2 Chain of Custody v1.1, §6.4.2 — mass-balancing options under the Credit Method (incl. Free Attribution)
• ISCC PLUS 203-2 v1.1, §7 — biogenic content by ¹⁴C (radiocarbon), independent of the CoC model
• ISCC Co-Processing guidance (ISCC PLUS guidance document)
WHAT IT IS
• ISCC handles bio + fossil FCC co-processing through its Chain of Custody. The biogenic fraction of outputs is determined by ¹⁴C analysis (203-2 §7); the certified bio-oil share is carried through the mass-balance / Credit Method (§6.4.2).
WHY IT’S BEING USED
• ISCC PLUS is the voluntary scheme with published free-attribution AND an existing US co-processing certified-refinery base (~5–6, vs 0 RSB) — coverage plus the partner availability the pathway needs.
KEY EQUATION / RULE
Credit Method: CF = (A_out ÷ A_in) × 100 ; A_credit = CF × A_certified-input (203-2 §6.4.2); biogenic carbon fixed by ¹⁴C (§7)

## Slide 10
STEP 8 OF 15 · Allocation of Refinery Emissions to Co-Products
Bolt-On — ISCC PLUS
NORMATIVE REFERENCE
• ISCC EU 205 v4.1, §4.3.8 — allocation of emissions to main & co-products by ENERGY content (mandatory)
• ISCC EU 205 v4.1, §4.3.5 — processing emissions (e_p)
WHAT IT IS
• Refinery processing emissions are allocated across the fuel co-products by energy content (§4.3.8) — each output carries an energy-share. This is ISCC’s mandatory basis, replacing RSB’s marginal virtual-baseline split.
WHY IT’S BEING USED
• Energy-content allocation is EU 205’s required method; using it now keeps the SAF CI consistent for eventual ISCC PLUS certification. Seam to document: the CDR root allocates by carbon mass at pyrolysis (Step 5) — the basis changes here.
KEY EQUATION / RULE
AF_product = LHV-energy(product) ÷ Σ LHV-energy(all outputs) (EU 205 §4.3.8)

## Slide 11
STEP 9 OF 15 · Allocation of Biogenic Carbon Attribute to Fuel Co-Products
Bolt-On — ISCC PLUS
NORMATIVE REFERENCE
• ISCC PLUS 203-2 v1.1, §6.4.2 — “Free Attribution Approach” under the Credit Method
WHAT IT IS
• Under Free Attribution the operator attributes the bio-oil’s certified sustainability characteristics to one or multiple outputs (e.g. SAF), irrespective of the proportion of certified input — within Chapter 6 guardrails (mass balance + conversion factors; capped at certified input × conversion).
WHY IT’S BEING USED
• Direct ISCC analog to RSB flexible attribution — lets the biogenic credit ride on the SAF output. ISCC chosen over RSB for US refinery availability; two published voluntary standards (ISCC PLUS, RSB Global) sanction the mechanism.
KEY EQUATION / RULE
Verbatim (203-2 §6.4.2): “System users can freely attribute the sustainability characteristics from the certified input(s) to one (or multiple) products… irrelevant of the proportion of the certified input material.”

## Slide 12
STEP 10 OF 15 · Transport of Fuel(s) to Blend Point
Charm CDR Methodology
NORMATIVE REFERENCE
• Transportation Emissions Accounting v1.1 §3.3 (Distance-Based, same as Steps 3 & 6); Appendix 1 (EF currency floors: pipeline ≤7 yr, ship ≤5 yr, road ≤3 yr)
WHAT IT IS
• Finished-fuel transport from refinery to blend point. Downstream of the CDR PDD boundary, so it borrows the Transportation module directly.
WHY IT’S BEING USED
• Same transport method used end-to-end; consistent EF sourcing rules across all legs.

## Slide 13
STEP 11 OF 15 · Quantification of Tree-to-Wake CI
Bolt-On — ISCC PLUS
NORMATIVE REFERENCE
• ISCC EU 205 v4.1, §4.3 — central CI formula (same structure as RSB; both RED-derived)
• IR (EU) 2022/996, Annex IX — standard emission factors; GWP CO₂=1, CH₄=28, N₂O=265
• GHG rides on the voluntary ISCC PLUS “GHG emissions” add-on (201 §2.4; 203-2 Annex I)
WHAT IT IS
• Aggregate lifecycle components into a CI: kgCO₂eq/dry-ton for the bio-oil intermediate, gCO₂eq/MJ for the final fuel. EFs from Annex IX (primary); grid electricity at the national-mix EF (§4.3.5.1) — no REC book-and-claim.
WHY IT’S BEING USED
• EU 205 is the GHG methodology in the ISCC PLUS document set (Overview v1.2, Table 1). Charm’s CI calculator already computes this from production data.
KEY EQUATION / RULE
E = e_ec + e_l + e_p + e_td + e_u − e_sca − e_ccs − e_ccr (EU 205 §4.3)

## Slide 14
STEP 12 OF 15 · Quantification of GHG Reduction vs Fossil Baseline
Bolt-On — ISCC PLUS
NORMATIVE REFERENCE
• ISCC EU 205 v4.1, §2 — GHG-savings requirement (RED III Art 31 thresholds; RED fossil comparator)
WHAT IT IS
• Saving % = (E_F − E) ÷ E_F × 100. Comparator per RED (EU 205 §2). [Exact comparator value TO CONFIRM from RED Annex V — not read this session; the RED transport comparator and the CORSIA aviation baseline differ.]
WHY IT’S BEING USED
• ISCC EU is RED-based, so savings anchor to the RED comparator. For a voluntary PLUS claim the pass/fail threshold is set by the destination market, not asserted here.
KEY EQUATION / RULE
Saving % = (E_F − E) ÷ E_F × 100

## Slide 15
STEP 13 OF 15 · Verification of Quantified Reductions
123Carbon (SFC MBM)
NORMATIVE REFERENCE
• SFC-SPEC-001 v01, §6.1.2 + §6.1.3 + §12 — third-party assessment for non-certified Solutions
• ISO 14064-3:2019 — verification/validation of GHG statements
WHAT IT IS
• SFC MBM requires a transparent, verifiable tracking system for minimum metrics, verified by independent third party; ISO 14064-3 is the established verification framework.
WHY IT’S BEING USED
• SFC MBM’s non-certified track drives the requirement; ISO 14064-3 is its normative framework.

## Slide 16
STEP 14 OF 15 · Credit Issuance on Registry
123Carbon (SFC MBM)
NORMATIVE REFERENCE
• SFC-SPEC-001 v01, §3.25 + §6.1.3 — Solution registration & Sustainability Profile
• 123Carbon registry protocols (format, unique ID, anti-double-counting ledger)
WHAT IT IS
• Sustainability Profile per credit: lifecycle EFs, LHV, feedstock type, production process, batch ID. Registry governs issuance format and the anti-double-counting ledger.
WHY IT’S BEING USED
• Registry issuance provides the double-counting protection for running parallel CDR and SAF accounting. (Registry may be 123Carbon or Isometric — Charm is in discussion with Isometric on hosting SAF attributes.)

## Slide 17
STEP 15 OF 15 · Credit Delivery, Retirement & Integrity
123Carbon (SFC MBM)
NORMATIVE REFERENCE
• SFC-SPEC-001 v01, §6.1.3 — non-certified Solution disclosure
• 123Carbon protocols — retirement, transfer chain, anti-double-counting
WHAT IT IS
• §6.1.3 requires non-certified Solutions to disclose underlying calculations, data sources and production processes in the buyer’s Report.
WHY IT’S BEING USED
• Binding disclosure obligation for non-certified Solutions; the methodology must produce all elements in transferable form.