## Slide 1
SAF Methodology Framework
Step-by-Step Normative References
Bio-Oil → FCC Co-Processing → SAF Credit | Charm Industrial | June 2026
Steps 1–6, 10 Charm CDR Methodology — validated PDD v1.12 (underlying Isometric protocols cited beneath)
Steps 7–9, 11–12 Bolt-On — Novel Methodology (RSB / ISCC normative references)
Steps 13–15 123 Carbon (SFC MBM Framework)

## Slide 2
Design Principles
One production system serving both carbon removal (CDR) and EACs — one architecture built from the most applicable parts of each.
1 An unusual dual mandate. Charm uses one production system to generate both CDR and EACs, as a business that began focused only on CDR. Neither the CDR-only nor the EAC-only methodologies is a perfect fit.
2 Both-and, not either-or. Charm's process is both-and, not either-or. The methodological architecture should match that structure by taking the best and most applicable aspects of CDR and EAC norms to build one dual-purpose structure.
3 One regime, not two. Running two separate accounting or supply-chain qualification regimes for a single production process is neither practical nor scalable.
4 Leverage the CDR investment. Charm has already invested heavily in validating its CDR projects under Isometric's rigorous requirements. That work should be leveraged as much as possible for EACs.

## Slide 3
Methodological Architecture
Biomass Qualification
Biomass Sourcing and Collection
Biomass Transport to Conversion Site
Biomass Conversion (Pyrolysis)
Allocation of Tree-to-Gate CI for pyro product feedstock
Counterfactual Storage excised for Fuels
Embodied Emissions excised for Fuels
Biochar Transport to Storage Site
Bio-Char Spreading
Verification of Bio-Char Removals
Credit Issuance on Registry
Credit delivery, retirement, management
Bio-Oil Transport to Injection Site
Bio-Oil Pre-Processing and Injection
Verification of Bio-Oil Removals
Credit Issuance on Registry
Credit delivery, retirement, management
Bio-Oil Transport to Refinery
Refinery co-processing into fuel products
Allocation of marginal refinery emissions to fuel products
Allocation of biogenic carbon attributes to fuel co-products
Transport of Fuel(s) to blend point
Quantification of Tree-to-Wheel CI for target fuel(s)
Quantification of GHG Reduction vs. Fossil Fuel baseline
Verification of Quantified Reductions
Credit Issuance on Registry
Credit delivery, retirement, management
Exciting Fourth Thing!
Some Stuff!
Other Stuff!
TBD!

## Slide 4
STEP 1 OF 15
Biomass Qualification
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, §B — Project Eligibility
Charm’s validated feedstock qualification — primary normative reference
Underlying: Biomass Feedstock Accounting v1.3, §2.1 — Sustainability Criteria
SC1–SC7, feedstock-type-specific; reviewed every Reporting Period
Underlying: Biomass Feedstock Accounting v1.3, §4.1 — Prohibited Feedstocks
Categorical gate: food/feed crops and purpose-grown BiCRS feedstocks have no path through the Module
Underlying: Biomass Feedstock Accounting v1.3, §4 — Market Leakage Emissions
Sourcing-driven market-shift assessment; valid 10 years
WHAT IT IS
• Three eligibility gates from BFA v1.3, all source-agnostic. (1) Sustainability Criteria SC1–SC7 (§2.1), feedstock-type-specific, reviewed every Reporting Period. (2) Prohibited Feedstocks — categorically ineligible regardless of other criteria. (3) Market Leakage (§4), sourcing-driven market-shift assessment, valid 10 years.
• Counterfactual Storage (§3) is the one gate excluded — it removes the durably-stored fraction from crediting, a removals concept with no role in a fuel-displacement claim
WHY IT'S BEING USED
• Provides a robust qualification program that ensures all feedstock is sourced responsibly and market leakage impacts are conservatively estimated
• Charm's CDR project already cleared these same gates under the PDD, so qualification is established precedent — the SAF claim reuses the determination rather than re-running it
• Isometric’s Biomass Feedstock Accounting module is uniquely tailored to qualifying woody biomass from wildfire fuels reduction efforts, which currently constitute the largest feedstock source for Charm

## Slide 5
STEP 2 OF 15
Biomass Sourcing and Collection
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, §B — Monitoring Plan
Charm’s validated supply-chain traceability — primary normative reference
Underlying: Biomass Feedstock Accounting v1.3, §2.1 + Appendix 1
Monitoring-plan requirements: feedstock origin, harvest authorization, species, mass per batch
RSB-STD-01-003-01 v3.2, §A.5
Zero-emission treatment for waste and residues up to point of collection (bolt-on citation)
WHAT IT IS
• BFA v1.3 §2.1 and Appendix 1 set the monitoring-plan framework: records of feedstock origin, harvest authorization,, and mass as well as collection emissions accounting for each supply-chain batch — source-agnostic, not tied to one biomass source
• Pre-collection-stage emissions are zero: wildfire fuel-reduction biomass qualifies as a waste/residue, and RSB §A.5 explicitly states "Waste and residues shall be considered to have zero emissions up to the process of collecting those materials"
• The methodology for accounting for emissions related to biomass collection activities is already elaborated in the validated PDD
WHY IT'S BEING USED
• The framework is reusable for the SAF claim and is already in place for Charm's CDR project, so no new sourcing documentation is needed
• Zero upstream emissions prior to the collection stage for wastes and residues aligns with both the PDD validated against Isometric’s requirements and RSB §A.5

## Slide 6
STEP 3 OF 15
Biomass Transport to Conversion Site
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, §B — Project Boundary & Monitoring Plan
As-validated transport legs and monitoring; emission factors are updated at least annually per the PDD
Underlying: Transportation Emissions Accounting v1.1, §3.3
Distance-Based Method: CO2e = D × W × EF
Underlying: Transportation Emissions Accounting v1.1, §3.4 + Appendix 1
EF currency floor: road ≤3 yr, rail ≤7 yr, most recent available; full fuel cycle required
WHAT IT IS
• The PDD sets the project boundary and monitoring plan for the truck and rail legs to the conversion site; the underlying Transportation module gives the Distance-Based calculation method (CO2e = distance × mass × mode-specific EF)
• Emission factors are currently updated at least annually per the PDD
WHY IT'S BEING USED
• Transport emissions quantification is already in Charm's validated PDD boundary; the same monitoring and calculation transfer to the SAF claim unchanged
• The underlying Transportation module explicitly covers multimodal freight, so rail and truck legs are both within scope under one reference

## Slide 7
STEP 4 OF 15
Biomass Conversion (Pyrolysis)
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, §B — Technical Description of Project Activity
Charm’s validated pyrolysis operation producing bio-oil — primary normative reference
Underlying: Bio-oil Geological Storage v1.2, §4 + §8.1
Applicability + Production Batch — biomass converted to bio-oil via pyrolysis
Underlying: Bio-oil Geological Storage v1.2, §8.5.5 + §8.5.6 —Emissions
Pyrolysis tailgas: CH₄ × GWP (Equation 10); testing per ASTM D7036 / ISO 17025
Underlying: Energy Use Accounting Module v1.3
Facility energy — electricity & stationary fuel, routed via §8.5.5
WHAT IT IS
• The pyrolysis step converts biomass to bio-oil — the SAF feedstock. Bio-oil Geological Storage v1.2 §4 and §8.1 frame this as the Production Batch; §8.5.6 quantifies direct pyrolysis emissions as tailgas CH₄ (CO₂ is not discounted, since the feedstock would have decayed within 15 years)
• Facility energy — pyrolysis start-up, reactor heating, supporting activity — is quantified via the Energy Use Accounting Module v1.3 (per §8.5.5). Tailgas emissions testing follows accredited stack testing (ASTM D7036 / ISO 17025) as required by Bio-Oil geological Storage v1.2
WHY IT'S BEING USED
• This is Charm’s existing validated conversion methodology — no new development. The same pyrolysis accounting that supports the CDR claim quantifies the bio-oil’s production-stage CI – Note: Amortization of embodied emissions associated with project capex is currently included in Production CI accounting. This will be changing later in the year, with embodied emissions amortized against gross removals generally; this will bring production accounting more into line with RSB — which under RSB-STD-01-003-01 v3.2 §A.5 excludes emissions from infrastructure and the manufacture of machinery and equipment — without creating the need for a parallel accounting system
• Bio-oil is the product carried forward to the refinery; the Bio-oil Geological Storage protocol governs how its conversion and direct emissions are measured

## Slide 8
STEP 5 OF 15
Allocation of Tree-to-Gate Emissions to Co-Products
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, Appendix 6 — GHG Statement Methodology (Calculations)
Carbon mass allocation of process emissions across co-products — Charm’s applied method
Underlying: GHG Accounting Module v1.1, §6.1
Co-product allocation framework
Bio-oil Geological Storage v1.2, §8.5.5.1
Co-product allocation requirement — routes to GHG Accounting Module §6.1
WHAT IT IS
• Charm allocates tree-to-gate process emissions between the co-products — biochar and the bio-oil fractions — on a carbon mass basis. The PDD lays this out in Appendix 6 (GHG Statement Methodology) as its applied reading of GHG Accounting Module v1.1 §6.1
• Carbon mass allocation is Charm’s chosen procedure; the protocol’s optional energy-content method is not used
WHY IT'S BEING USED
• This keeps the SAF co-product accounting identical to the validated CDR treatment on the same physical pyrolysis process

## Slide 9
STEP 6 OF 15
Bio-Oil Transport to Refinery
Existing CDR Methodology
NORMATIVE REFERENCE
Charm PDD v1.12, §B — Project Boundary & Monitoring Plan
The validated transport-accounting method Charm applies to bio-oil shipment legs
Underlying: Transportation Emissions Accounting v1.1, §3.3
Distance-Based Method: CO2e = D × W × EF (rail + truck)
Underlying: Transportation Emissions Accounting v1.1, §3.4 + Appendix 1
EF currency floor: road ≤3 yr, rail ≤7 yr, most recent available; full fuel cycle required
WHAT IT IS
• The bio-oil shipment to the FCC refinery uses the same transport-accounting method Charm's PDD validates for bio-oil movement — Calculated as distance × mass × mode-specific EF. The refinery endpoint is SAF-specific, but the method is unchanged
• Emission factors are currently updated at least annually per the PDD
WHY IT'S BEING USED
• The transport-accounting method is already validated in Charm's CDR PDD; only the destination differs for the SAF pathway, so the calculation carries over without new methodology
• Using the same underlying Transportation module across all bio-oil transport legs keeps the methodology internally consistent and simplifies verifier review

## Slide 10
STEP 7 OF 15
Refinery Co-Processing into Fuel Co-Products
Bolt-On — Novel
NORMATIVE REFERENCE
RSB-STD-01-010 v2.8, §2.4
Requirements for co-processing biogenic and fossil feedstocks — three documentation options
RSB-STD-01-010 v2.8, Annex IV
Optional flexible attribution methodology — eligible-carbon and advanced-fuel calculation (Eq [1]–[2])
WHAT IT IS
• RSB §2.4 establishes three options for documenting biogenic fractions in co-processing: mass balance (§2.4.3), radiocarbon analysis (§2.4.4), or flexible attribution (§2.4.5)
• Annex IV sets out the flexible-attribution calculation: identify the eligible biogenic carbon exiting the unit (Eq [1]), then the advanced-fuel volume it supports (Eq [2], detail in Step 9)
WHY IT'S BEING USED
• RSB has a highly developed, published normative framework specifically for FCC-style co-processing of biogenic and fossil feedstocks — this is the coverage gap that the existing Isometric modules do not address
• Flexible attribution (§2.4.5) is the pathway that enables free designation of which output receives the biogenic carbon credit in Step 9; this step establishes the normative basis for that attribution
KEY EQUATION · RSB-STD-01-010 v2.8, Annex IV [1]
Output_elig.C = m_elig.f × Carbon-content_elig.f × η_C,i
where: Output_elig.C = eligible (biogenic) carbon exiting the unit (t C); m_elig.f = eligible feedstock entering (t, dry); Carbon-content_elig.f = its carbon content (% w/w); η_C,i = carbon conversion efficiency (% of input C ending in the product)

## Slide 11
STEP 8 OF 15
Allocation of Marginal Refinery Emissions to Co-Products
Bolt-On — Novel
NORMATIVE REFERENCE
RSB-GUI-PG-2025-02 §6.1 — Co-Processing GHG Calculation
Virtual baseline split: shared process energy by inlet energy fraction; biogenic-specific inputs attributed entirely to the biofuel
WHAT IT IS
• Co-processing emissions use a virtual baseline split: shared refinery process energy is allocated to the biofuel by its inlet energy fraction, F_bio ÷ (F_bio + F_fossil)
• Inputs specific to the biogenic feedstock — extra hydrogen for deoxygenation, additional heat and reagents — are attributed entirely to the biofuel (the e_additional term), measured against the fossil-only baseline rather than energy-split
WHY IT'S BEING USED
• Published normative formula with explicit variables and a defined calculation — fully auditable by any verifier familiar with RSB
• Physically grounded and marginal: shared load is split by energy, while emissions caused specifically by adding the biogenic feedstock fall to the biofuel — the counterfactual logic RSB co-processing requires
KEY EQUATION · RSB-GUI-PG-2025-02 §6.1 (Co-Processing GHG)
e_processing = E_total × [F_bio ÷ (F_bio + F_fossil)] + e_additional
where: E_total = baseline process emissions shared by fossil & biogenic inputs; F_bio ÷ (F_bio + F_fossil) = biogenic feedstock’s inlet energy fraction (allocates the shared process emissions); e_additional = energy/reagents (extra H₂, heat) specifically required for the biogenic feedstock — attributed entirely to the biofuel

## Slide 12
STEP 9 OF 15
Allocation of Biogenic Carbon Credit to Fuel Co-Products
Bolt-On — Novel
NORMATIVE REFERENCE
RSB-STD-01-010 v2.8, §2.4.5 + Annex IV [1]–[3]
Flexible (free) attribution — normative requirement and three-step calculation
WHAT IT IS
• RSB §2.4.5 is the normative requirement: the operator designates which output receives the biogenic carbon attribute. Annex IV formulas [1]–[3] calculate: (1) eligible carbon output, (2) attributed advanced fuel volume, (3) GHG intensity per MJ of that SAF
WHY IT'S BEING USED
• Free attribution is the mechanism that makes SAF credit economics viable for FCC co-processing: operator can designate the SAF output as the recipient of the full bio-oil biogenic carbon credit, rather than spreading it across all refinery outputs by mass or energy fraction
KEY EQUATION · RSB-STD-01-010 v2.8, Annex IV [2] & [5]
[2] TS_adv.fuel = Output_elig.C × Output carbon-content
[5] AF [%] = LHV_af ÷ Total energy output [MJ]
where: TS_adv.fuel = advanced-fuel volume eligible for the claim (t, dry); Output_elig.C = eligible carbon from [1] (t C); Output carbon-content = carbon content of the fuel (t fuel per t C); AF = energy-basis allocation factor to the advanced fuel (%); LHV_af = LHV of the advanced fuel (MJ/t); Total energy output = LHV summed across all output products (MJ)

## Slide 13
STEP 10 OF 15
Transport of Fuel(s) to Blend Point
Existing CDR Methodology
NORMATIVE REFERENCE
Transportation Emissions Accounting v1.1, §3.3
Distance-Based Method: CO2e = D × W × EF (same as Steps 3 and 6)
Transportation Emissions Accounting v1.1, Appendix 1
EF currency floor (Appendix 1): pipeline ≤7 yr, ship ≤5 yr, road ≤3 yr; most recent available
WHAT IT IS
• Quantifies finished-fuel transport from the refinery to the blend point. This leg is downstream of Charm's CDR PDD boundary, so it borrows the Transportation Emissions Accounting method rather than routing through the PDD
• Appendix 1 sets the EF-currency floor by mode (pipeline ≤7 yr, ship ≤5 yr, road ≤3 yr) — all relevant for downstream SAF logistics depending on refinery location and blend point
WHY IT'S BEING USED
• No new methodology work: the same transport-accounting method used upstream applies to the downstream fuel leg, even though this leg sits outside the validated CDR boundary
• Using one transport method across all legs keeps EF sourcing rules and calculations consistent end-to-end

## Slide 14
STEP 11 OF 15
Quantification of Tree-to-Wheel CI
Bolt-On — Novel
NORMATIVE REFERENCE
RSB-STD-01-003-01 v3.2, §B.1
Well-to-wake central formula: E = eec + el + ep + etd + eu − esca − eccs − eccr
RSB-STD-01-003-01 v3.2, §A.1
Functional unit
WHAT IT IS
• §B.1 central formula aggregates all lifecycle components into a single CI in gCO₂eq/MJ (LHV, dry basis); §A.2 sets the well-to-wake system boundary for aviation biofuels
• §A.5 emission-factor sourcing: EU Annex IX standard values primary, national emission factors secondary, Ecoinvent/peer-reviewed LCA databases tertiary. GWP (AR5): CO₂=1, N₂O=265, CH₄=28
WHY IT'S BEING USED
• Published normative formula with defined functional unit, GWP values, and system boundary — provides auditable structure for aggregating the Isometric-derived upstream CI components into the SAF CI metric
• Aligns end product with industry standards
KEY EQUATION · RSB-STD-01-003-01 v3.2, §B.1
E = e_ec + e_l + e_p + e_td + e_u − e_sca − e_ccs − e_ccr
where: E = total fuel CI (g CO₂eq/MJ); e_ec = extraction/cultivation; e_l = land-use-change (annualised); e_p = processing; e_td = transport & distribution; e_u = fuel in use; e_sca = soil-carbon savings; e_ccs = carbon capture & geological storage savings; e_ccr = carbon capture & replacement savings

## Slide 15
STEP 12 OF 15
Quantification of GHG Reductions vs. Fossil Fuel Baseline
Bolt-On — Novel
NORMATIVE REFERENCE
RSB-STD-01-003-01 v3.2, §A.9 + Table 2
GHG savings formula; fossil comparator = 90 gCO₂eq/MJ (well-to-wake)
RSB-STD-01-003-02 v2.1, Executive Summary + Table 1 (pp. 6–7) Fossil fuel baseline calculation methodology — aviation kerosene
WHAT IT IS
• Saving [%] = (E_F − E) ÷ E_F × 100; RSB Global fossil comparator for biofuels = 90 gCO₂eq/MJ, confirmed in RSB-STD-01-003-01 v3.2 Table 2 (effective June 2025)
• RSB-STD-01-003-02 derives the 90 gCO₂eq/MJ fossil baseline from a lifecycle analysis of conventional jet fuel production and combustion
WHY IT'S BEING USED
• 90 gCO₂eq/MJ is the most widely cited SAF fossil baseline and provides a credible, verifier-recognized anchor even if RSB certification is not ultimately pursued
• Publishing the % reduction vs. this baseline gives buyers a number they can benchmark against other SAF products; the RSB methodology is publicly available and verifiable without a certification body
KEY EQUATION · RSB-STD-01-003-01 v3.2, §A.9 + Table 2
Saving [%] = (E_F − E) ÷ E_F × 100
where: Saving = GHG reduction vs the fossil baseline (%); E = fuel CI (g CO₂eq/MJ); E_F = fossil comparator = 90 g CO₂eq/MJ (RSB GLOBAL biofuel, Table 2)

## Slide 16
STEP 13 OF 15
Verification of Quantified Reductions
123 Carbon
NORMATIVE REFERENCE
SFC-SPEC-001 v01, §6.1.2 + §6.1.3 + §12
Third-party assessment requirements for non-certified Solutions
ISO 14064-3:2019
Requirements and guidance for verification and validation of GHG statements
WHAT IT IS
• SFC MBM §6.1.2 and §6.1.3 requires a transparent and verifiable tracking system for minimum metrics to be verified with independent third-party assessment; §12 allows optional Report verification
• ISO 14064-3:2019 is the international standard for third-party verification of GHG statements — defines verifier requirements, procedures, and statement of assurance
WHY IT'S BEING USED
• SFC MBM's non-certified track criteria drive the verification requirement; §6.1.2+3 is the binding obligation and ISO 14064-3 is its established normative framework

## Slide 17
STEP 14 OF 15
Credit Issuance on Registry
123 Carbon
NORMATIVE REFERENCE
SFC-SPEC-001 v01, §3.25 + §6.1.3
Solution registration and Sustainability Profile (§3.25) requirements
123 Carbon registry protocols
Credit format, unique identifier assignment, and anti-double-counting ledger
WHAT IT IS
• SFC MBM §3.25 defines the Sustainability Profile that must accompany each credit: lifecycle GHG emission factors, LHV, feedstock type, production process, batch ID
• 123 Carbon registry governs credit issuance format, unique identifier assignment, and the ledger that prevents double-counting across credit streams
WHY IT'S BEING USED
• 123 Carbon is the named registry; SFC MBM §3.25 and §6.1.3 define exactly what information must appear on each credit at issuance — the methodology must be designed to produce all these outputs at batch level
• Registry-level issuance provides the double-counting protection required for running parallel CDR and SAF accounting on the same production process

## Slide 18
STEP 15 OF 15
Credit Delivery, Retirement, and Integrity
123 Carbon
NORMATIVE REFERENCE
SFC-SPEC-001 v01, §6.1.3
Non-certified Solution disclosure requirements
123 Carbon protocols
Credit retirement, transfer chain, and anti-double-counting provisions
WHAT IT IS
• §6.1.3 requires non-certified Solutions to disclose underlying calculations, data sources, and production processes in the buyer's Report
WHY IT'S BEING USED
• §6.1.3 is the binding disclosure obligation for non-certified Solutions — the methodology must produce all required elements in a form that is documentable and transferable to the buyer
• Anti-double-counting provisions protect Charm and the buyer from the primary integrity risk: the same GHG reduction claimed simultaneously in both the CDR and SAF credit streams