## Slide 1
Free Allocation of Sustainability Attributes
How RSB and ISCC Treat It, and Why

## Slide 2
1
Two premier certification systems, one shared design choice
RSB (Roundtable on Sustainable Biomaterials) and ISCC (International Sustainability & Carbon Certification) are the two leading global certification systems governing sustainability attributes for renewable fuels — the ones that determine whether a biogenic claim on a barrel of fuel is credible.
Both organizations run more than one certification track. This matters because the tracks disagree with each other on a specific question:
Can the biogenic share of a co-processed or blended fuel be assigned freely to one output stream — rather than spread proportionally across every output — as long as the total assigned never exceeds the physical amount actually present?
The answer depends entirely on which track within each body is in play.

## Slide 3
2
The CORSIA track: no free allocation, in either system
Both RSB and ISCC offer a certification option built specifically for ICAO's CORSIA aviation program. Neither allows free allocation there — because CORSIA's own accounting rules don't.
RSB Standard for ICAO CORSIA
RSB-STD-12-001, v1.7, April 2026, §3.4.7.1, p.23
“...energy-based allocation shall be used to assign emission burdens to all co-products in proportion to their contribution to the total energy content... of products and co-products.”
ISCC CORSIA 203, Traceability and Chain of Custody
Version 2.0, §4.4.4 Co-Processing, p.42
“For all three approaches [energetic determination, efficiency/loss determination, or ¹⁴C analysis], free attribution of the sustainable share to outgoing products is not allowed.”
This is a boundary condition, not the main story. Both bodies also run a separate, voluntary track — and that's where free allocation lives.

## Slide 4
However —
both RSB and ISCC also run voluntary certification pathways that explicitly allow free allocation.
RSB Standard for Advanced Fuels | ISCC PLUS

## Slide 5
3
How RSB's free allocation works
RSB Standard for Advanced Fuels (RSB-STD-01-010 v2.8, §2.4.2, p.11) offers flexible attribution as one of three ways to document a biogenic/fossil split — alongside mass balance and the radiocarbon method.
Worked example, from the standard itself (Annex IV, p.29):
“1.1t of jet fuel will be sold with 100% bioattributed claim, while the remaining quantity of products will be sold with 0% bioattributed claim. Note that the amount of jet fuel sold with 100% flexible attributed claim is limited by the amount of biogenic carbon content in the biobased feedstock considering the efficiency in converting the feedstock into output.”
The cap (Annex IV, p.26): eligible carbon exiting the process = feedstock mass × carbon content × conversion efficiency. Worked figure: 10t of biogenic carbon in, at 90% conversion efficiency, yields a 9t ceiling — regardless of which output the claim is pointed at.
Guardrails: GHG emissions still allocated energy-basis regardless of the claim (Annex IV, Note 7, p.28); non-negative balance every 3 months (§2.4.5, p.12); output cannot claim “physical sustainable content” — an alternate label like “RSB-Compliant Advanced Fuel” is required instead (§2.5.4, p.12).
RSB-STD-01-010 v2.8, §2.4.2, §2.4.5, §2.5.4, Annex IV, pp.11, 12, 26, 28, 29.

## Slide 6
4
How ISCC's free allocation works
ISCC PLUS 203-2, Chain of Custody v1.1 (valid 13 Nov 2025), §6.4.2, p.26, lists four mass-balancing options under its Credit Method — Free Attribution, Fuel-Use Excluded, Proportional, and Trace-the-Atom — and defines the first:
“Under Free Attribution Approach, the system user can attribute the sustainability characteristics from the certified input materials to the products... This attribution can be done irrelevant of the proportion of the certified input material to the other inputs... System users can freely attribute the sustainability characteristics from the certified input(s) to one (or multiple) products.”
Guardrails (§6.3, p.21 — apply to every mass-balancing option, Free Attribution included):
• Physical output: “The amount of attributable credits cannot be higher than the physical output... It is not possible to attribute to a quantity of output which is not produced at the site.”
• Chemical connectivity (§6.1, pp.17–18): the standard requires “the theoretical possibility of chemically converting the certified input(s) to the output(s)” plus real production infrastructure — so outputs must plausibly contain the certified input's molecules, not just carry a bookkeeping label.
• Operational data: every input, output, loss, and conversion factor behind the claim “shall be collected and documented” and valid for the audit period — not asserted after the fact.
• Site-specific: mass balance runs per physical site — “company level mass balance is not possible.”
• Disclosure (§6.4.2, p.27): where an output's certified share is “compensated” beyond the proportion of certified input actually used, the outgoing Sustainability Declaration must say so.
ISCC PLUS 203-2 Chain of Custody v1.1, §6.1, §6.3, §6.4.2, pp.17–18, 21, 26–27.

## Slide 7
5
Why two independent standard-setters built the same tool
Both mechanisms start from the same physical fact. Co-processing and blending physically commingle biogenic and fossil material before any output stream exists. ISCC states the consequence directly (§6.2, p.18):
“Due to the physical mixing, the mixture loses its individual properties. The sustainability characteristics of materials can therefore only be determined via the bookkeeping.”
Once that's true, spreading the biogenic claim proportionally across every output — including the lowest-value ones — is a bookkeeping choice, not a more physically accurate one. Concentrating that same, already-fixed quantity onto the highest-value stream is an equally valid bookkeeping choice, provided it never exceeds what's physically present. Both standards enforce exactly that cap (RSB Annex IV Step 1; ISCC §6.3 “Physical Output”), and both keep it separate from the underlying emissions math and from double counting.
That is the reading this comparison supports: for the industry's two leading certifiers, free allocation is not really an “if” question anymore — it's a “when and how” question, bounded by a hard physical cap. What it buys is commercial: it lets a supplier concentrate a fixed, already-capped biogenic quantity onto the co-product stream the market values most (e.g. SAF), which is what makes bolting biogenic feedstock onto existing fossil infrastructure viable at the scale decarbonization targets require — without the total claimed benefit ever exceeding what was physically put in.
Synthesis drawn from the guardrails cited on slides 5–6: RSB-STD-01-010 v2.8 Annex IV; ISCC PLUS 203-2 v1.1 §6.2–6.3.

## Slide 8
6
Guardrails, side by side
Guardrail | RSB Advanced Fuels | ISCC PLUS
Physical cap on the claim | Capped by feedstock carbon content × conversion efficiency (Annex IV, p.26) | “Attributable credits cannot be higher than the physical output” (§6.3, p.21)
Emissions math unaffected | GHG emissions still allocated energy-basis regardless of claim (Annex IV, Note 7, p.28) | Attribution governs the credit/claim; not shown here to alter GHG accounting
Disclosure requirement | Alternate claim label required — no “physical sustainable content” claim (§2.5.4, p.12) | Outgoing Sustainability Declaration must flag compensation beyond proportion (§6.4.2, p.27)
Balance / bookkeeping | Non-negative balance every 3 months, documented (§2.4.5, p.12) | Site-specific mass balance, documented operational data (§6.3, p.21)
Status | Published, in-force methodology with a numeric worked example (Annex IV) | Published, in-force methodology (203-2 v1.1, valid 13 Nov 2025)
See slides 5–6 for full quotes and the citation appendix for the complete source list.

## Slide 9
7
The answer, in one table
 | RSB | ISCC
CORSIA track | No free allocation (RSB-STD-12-001 v1.7, §3.4.7.1, p.23) | No free allocation (ISCC CORSIA 203 v2.0, §4.4.4, p.42)
Voluntary track | Free allocation allowed (RSB-STD-01-010 v2.8, Annex IV) | Free allocation allowed (ISCC PLUS 203-2 v1.1, §6.4.2)
Common guardrail | Capped at physically-present biogenic carbon; emissions stay energy-allocated | Capped at physical output; compensation beyond proportion must be disclosed
Two independent, premier certification bodies drew the identical line: proportional-only where a binding regulatory scheme (CORSIA) requires it, free allocation where the market is voluntary — bounded by the same style of physical cap in both cases.
Full citations in the appendix.

## Slide 10
Appendix A
Sources
RSB Standard for Advanced Fuels, RSB-STD-01-010, Version 2.8, published April 2026.
Cited: §2.4.2 (p.11), §2.4.5 (p.12), §2.5.4 (p.12), Annex IV (pp.26, 28, 29).
RSB Standard for ICAO CORSIA, RSB-STD-12-001, Version 1.7, published April 2026.
Cited: §3.4.7.1 (p.23).
ISCC PLUS 203-2, Chain of Custody, Version 1.1, valid from 13 November 2025.
Cited: §6.1 (pp.17–18), §6.2 (p.18), §6.3 (p.21), §6.4.2 (pp.26–27).
ISCC CORSIA 203, Traceability and Chain of Custody, Version 2.0.
Cited: §4.4.4 Co-Processing (p.42).
Not checked in this review: EU RED, LCFS, ISCC EU (the DR 2023/1640-scoped track, distinct from ISCC PLUS).

## Slide 11
Backup
Numeric detail held in reserve for follow-up questions

## Slide 12
Backup 1
RSB Annex IV — the physical cap, in numbers
From the standard's own Figure 1 (Annex IV, p.29):
• Inputs: 21t biomass feedstock (10t biogenic carbon) + 98t fossil feedstock (68.6t fossil carbon)
• Process conversion efficiency: 90%
• Outputs: 1.1t SAF (carrying 0.9t of the attributed biogenic carbon), 2.4t fossil-based jet fuel (2.1t fossil carbon attributed), plus other fossil-based products (59.7t fossil carbon attributed)
• Resulting carbon footprint: 0.98 tCO2eq/t SAF vs. 1.69 tCO2eq/t fossil jet fuel
Note in the figure: “the input of biogenic carbon is 1t. The output of biogenic carbon attributed to the final product is 0.9t since a conversion efficiency of 90% was considered.”
RSB-STD-01-010 v2.8, Annex IV, Figure 1 and accompanying text, p.26 and p.29.

## Slide 13
Backup 2
RSB Annex V — flexible attribution of process inputs
Annex V (added in v2.8, p.30) extends flexible attribution beyond the biogenic feedstock itself to process inputs and utilities (electricity, steam, oxygen) in a co-processing SAF example.
Worked comparison (p.32):
• Without flexible attribution of inputs: SAF GHG intensity = 68 g CO2e/MJ
• With flexible attribution of inputs: SAF GHG intensity = 30.25 g CO2e/MJ
Guardrail (Step 3, p.32): “You may not attribute more of an input than the amount... used in the co-process.” Low-carbon inputs are attributed first, up to their actual available quantity.
RSB-STD-01-010 v2.8, Annex V, pp.30–32.

## Slide 14
Backup 3
ISCC PLUS — the mass-balance foundation under Free Attribution
Chemical connectivity (§6.1, pp.17–18) — the precondition for any attribution, Free Attribution included: “Chemical link: the theoretical possibility of chemically converting the certified input(s) to the output(s)” plus “Process feasibility: availability of technical infrastructure.” Where both hold, “process outputs (products) can contain molecules or atoms of the certified input.”
General mass-balance rule (§6.2, p.18): “Under mass balance, the physical mixing of material with different sustainability characteristics and the mixing of certified and non-certified material is allowed, while ensuring that the sustainability characteristics remain assigned to physical batches of material on a bookkeeping basis.”
Four options under the Credit Method (Figure 6, p.26): Free Attribution, Fuel-Use Excluded Attribution, Proportional Attribution, Trace-the-Atom — each usable within the same §6.3 guardrails.
ISCC PLUS 203-2 Chain of Custody v1.1, §6.1–6.2, pp.17–18, 26.