## Slide 1
Free Allocation of Sustainability Attributes
How RSB and ISCC Treat It, and Why

## Slide 2
1
Two premier certification systems, one shared design choice
RSB (Roundtable on Sustainable Biomaterials) and ISCC (International Sustainability & Carbon Certification) are the two leading global certification systems governing sustainability attributes for renewable fuels — the ones that determine whether a biogenic claim on a barrel of fuel is credible.
Both organizations run more than one certification track. This matters because the tracks disagree with each other on a specific question:
Can the biogenic share of a co-processed or blended fuel be assigned freely to one output stream — rather than spread proportionally across every output — as long as the total assigned never exceeds the physical amount actually present?
The answer depends entirely on which track within each body is in play.

## Slide 3
2
The CORSIA track: no free allocation, in either system
Both RSB and ISCC offer a certification option built specifically for ICAO's CORSIA aviation program. Neither allows free allocation there — because CORSIA's own accounting rules don't.
RSB Standard for ICAO CORSIA
RSB-STD-12-001, v1.7, April 2026, §3.4.7.1, p.23
“...energy-based allocation shall be used to assign emission burdens to all co-products in proportion to their contribution to the total energy content... of products and co-products.”
ISCC CORSIA 203, Traceability and Chain of Custody
Version 2.0, §4.4.4 Co-Processing, p.42
“For all three approaches [energetic determination, efficiency/loss determination, or ¹⁴C analysis], free attribution of the sustainable share to outgoing products is not allowed.”
This is a boundary condition, not the main story. Both bodies also run a separate, voluntary track — and that's where free allocation lives.

## Slide 4
However —
both RSB and ISCC also run voluntary certification pathways that explicitly allow free allocation.
RSB Standard for Advanced Fuels | ISCC PLUS

## Slide 5
3
How RSB's free allocation works
RSB Standard for Advanced Fuels (RSB-STD-01-010 v2.8, §2.4.2, p.11) offers flexible attribution as one of three ways to document a biogenic/fossil split — alongside mass balance and the radiocarbon method.
Worked example (Annex IV, p.29): “1.1t of jet fuel will be sold with 100% bioattributed claim, while the remaining quantity of products will be sold with 0% bioattributed claim... limited by the amount of biogenic carbon content in the biobased feedstock considering the efficiency in converting the feedstock into output.” The cap (Annex IV, p.26): eligible carbon = feedstock mass × carbon content × conversion efficiency — 10t of biogenic carbon in, at 90% conversion, yields a 9t ceiling.
Guardrails (§2.4.5, p.12 — all four are numbered requirements in the standard itself):
• Documentation: must record “the amount of bio-based or eligible non-biogenic feedstock... used as material,” “the carbon content (%, w/w)... entering the industrial process,” and “the quantification of losses, by mass... for each lost material.”
• Book-keeping system: “a documented book-keeping system in place to monitor the balance of bio-based or eligible non-biogenic feedstock that have been added to the system and advanced fuel withdrawn from the system.”
• Balance period: claims “balanced within a 3-month period” — a deficit may occur mid-period, but “a non-negative balance is achieved over the 3-months-period.”
• Site boundary: one site, connected sites on the same pipeline/transport network, or separate sites only “if the operator can ensure and demonstrate... that double-booking does not occur.”
• Emissions unaffected (Annex IV, Note 7, p.28): “Allocation of the GHG emissions among the outputs shall be performed on an energy basis” regardless of the claim.
• Claim-label restriction (§2.5.4, p.12): output cannot claim “physical sustainable content” — an alternate label like “RSB-Compliant Advanced Fuel” is required instead.
RSB-STD-01-010 v2.8, §2.4.2, §2.4.5, §2.5.4, Annex IV, pp.11, 12, 26, 28, 29.

## Slide 6
4
How ISCC's free allocation works
ISCC PLUS 203-2, Chain of Custody v1.1 (valid 13 Nov 2025), §6.4.2, p.26, lists four mass-balancing options under its Credit Method — Free Attribution, Fuel-Use Excluded, Proportional, and Trace-the-Atom — and defines the first:
“Under Free Attribution Approach, the system user can attribute the sustainability characteristics from the certified input materials to the products... This attribution can be done irrelevant of the proportion of the certified input material to the other inputs... System users can freely attribute the sustainability characteristics from the certified input(s) to one (or multiple) products.”
Guardrails (§6.3, p.21 — apply to every mass-balancing option, Free Attribution included):
• Physical output: “The amount of attributable credits cannot be higher than the physical output... It is not possible to attribute to a quantity of output which is not produced at the site.”
• Chemical connectivity (§6.1, pp.17–18): the standard requires “the theoretical possibility of chemically converting the certified input(s) to the output(s)” plus real production infrastructure — so outputs must plausibly contain the certified input's molecules, not just carry a bookkeeping label.
• Operational data: every input, output, loss, and conversion factor behind the claim “shall be collected and documented” and valid for the audit period — not asserted after the fact.
• Site-specific: mass balance runs per physical site — “company level mass balance is not possible.”
• Disclosure (§6.4.2, p.27): where an output's certified share is “compensated” beyond the proportion of certified input actually used, the outgoing Sustainability Declaration must say so.
ISCC PLUS 203-2 Chain of Custody v1.1, §6.1, §6.3, §6.4.2, pp.17–18, 21, 26–27.

## Slide 7
5
Why two independent standard-setters built the same tool
Proportional allocation via ¹⁴C testing is a genuine attempt to measure biogenic content physically — not arbitrary bookkeeping, and why a binding scheme like CORSIA requires it. But the measurement runs into a real limit at the blend rates co-processing actually operates at. ISCC's own guidance concedes this (“Detection of low bio-content,” p.14):
“When relatively small fractions of biomass inputs are co-processed, and the biomass feedstock undergoes multiple processing steps, the amount of bio-content that end up in the co-processed output might be lower than the detection limits of the radiocarbon testing method used.” Their fix — ASTM D6866, treat anything under 0.5 pMC as zero — is a tacit admission that the “more physically accurate” method can't resolve the signal at the low blend ratios (bio-oil typically enters at ≤5%) co-processing runs at.
The sharper reason free allocation exists is economic. Markets price the scarce thing highest. Forcing a fixed quantity of biogenic content to spread proportionally across every co-product output dilutes it below the concentration any single stream needs to matter as a decarbonization claim — including the one stream where the demand actually is (SAF, for a hard-to-abate sector like aviation). Free allocation lets that same, capped physical quantity concentrate into the stream the market values most, without changing the total fossil carbon displaced system-wide.
This is book-and-claim — the same mechanism class behind renewable energy certificates. What makes it legitimate isn't molecule-level tracing, which both standards' own documents show is tenuous at real-world blend ratios; it's the guardrails that keep the claim conservative and verifiable: a hard physical cap on the total quantity claimed (RSB Annex IV; ISCC §6.3 “Physical Output”), and mandatory disclosure when a claim departs from strict proportionality.
For a market-based mechanism to scale to what decarbonization targets in hard-to-abate sectors require, it has to be allowed to actually function as a market — concentrating a fixed, physically-capped benefit into its highest-value use — provided the atmospheric-impact claim stays conservative and verifiable. That is what free allocation is built to do, and why two independent certifiers converged on it.
RSB-STD-01-010 v2.8 Annex IV; ISCC PLUS 203-2 v1.1 §6.3; ISCC Questions and Answers on Co-Processing v1.0, p.14.

## Slide 8
6
Guardrails, side by side
Guardrail | RSB Advanced Fuels | ISCC PLUS
Physical cap on the claim | Capped by feedstock carbon content × conversion efficiency (Annex IV, p.26) | “Attributable credits cannot be higher than the physical output” (§6.3, p.21)
Emissions accounting | Confirmed unaffected by the claim — still allocated energy-basis (Annex IV, Note 7, p.28) | Governed separately, as a voluntary add-on distinct from this Chain of Custody chapter (201 §2.4, p.24); whether attribution choice affects the add-on's own GHG calculation was not checked
Disclosure requirement | Alternate claim label required — no “physical sustainable content” claim (§2.5.4, p.12) | Outgoing Sustainability Declaration must flag compensation beyond proportion (§6.4.2, p.27)
Balance / bookkeeping | Non-negative balance every 3 months, documented (§2.4.5, p.12) | Site-specific mass balance, documented operational data (§6.3, p.21)
Status | Published, in-force methodology with a numeric worked example (Annex IV) | Published, in-force methodology (203-2 v1.1, valid 13 Nov 2025)
See slides 5–6 for full quotes and the citation appendix for the complete source list.

## Slide 9
7
The answer, in one table
 | RSB | ISCC
CORSIA track | No free allocation (RSB-STD-12-001 v1.7, §3.4.7.1, p.23) | No free allocation (ISCC CORSIA 203 v2.0, §4.4.4, p.42)
Voluntary track | Free allocation allowed (RSB-STD-01-010 v2.8, Annex IV) | Free allocation allowed (ISCC PLUS 203-2 v1.1, §6.4.2)
Common guardrail | Capped at physically-present biogenic carbon; emissions stay energy-allocated | Capped at physical output; compensation beyond proportion must be disclosed
Two independent, premier certification bodies drew the identical line: proportional-only where a binding regulatory scheme (CORSIA) requires it, free allocation where the market is voluntary — bounded by the same style of physical cap in both cases.
Full citations in the appendix.

## Slide 10
Appendix A
Sources
RSB Standard for Advanced Fuels, RSB-STD-01-010, Version 2.8, published April 2026.
Cited: §2.4.2 (p.11), §2.4.5 (p.12), §2.5.4 (p.12), Annex IV (pp.26, 28, 29).
RSB Standard for ICAO CORSIA, RSB-STD-12-001, Version 1.7, published April 2026.
Cited: §3.4.7.1 (p.23).
ISCC PLUS 203-2, Chain of Custody, Version 1.1, valid from 13 November 2025.
Cited: §6.1 (pp.17–18), §6.2 (p.18), §6.3 (p.21), §6.4.2 (pp.26–27).
ISCC PLUS 201, System Basics, Version 1.1, valid from 13 November 2025.
Cited: §2.4 Voluntary Add-Ons under ISCC PLUS (p.24) — establishes that GHG/CI reporting sits outside the Chain of Custody chapter cited above, as a separate voluntary add-on.
ISCC CORSIA 203, Traceability and Chain of Custody, Version 2.0.
Cited: §4.4.4 Co-Processing (p.42).
Not checked in this review: EU RED, LCFS, ISCC EU (the DR 2023/1640-scoped track, distinct from ISCC PLUS), and whether ISCC PLUS's GHG add-on calculation is affected by which mass-balancing option is used.

## Slide 11
Backup
Numeric detail held in reserve for follow-up questions

## Slide 12
Backup 1
RSB Annex IV — the physical cap, in numbers
From the standard's own Figure 1 (Annex IV, p.29):
• Inputs: 21t biomass feedstock (10t biogenic carbon) + 98t fossil feedstock (68.6t fossil carbon)
• Process conversion efficiency: 90%
• Outputs: 1.1t SAF (carrying 0.9t of the attributed biogenic carbon), 2.4t fossil-based jet fuel (2.1t fossil carbon attributed), plus other fossil-based products (59.7t fossil carbon attributed)
• Resulting carbon footprint: 0.98 tCO2eq/t SAF vs. 1.69 tCO2eq/t fossil jet fuel
Note in the figure: “the input of biogenic carbon is 1t. The output of biogenic carbon attributed to the final product is 0.9t since a conversion efficiency of 90% was considered.”
RSB-STD-01-010 v2.8, Annex IV, Figure 1 and accompanying text, p.26 and p.29.

## Slide 13
Backup 2
RSB Annex V — flexible attribution of process inputs
Annex V (added in v2.8, p.30) extends flexible attribution beyond the biogenic feedstock itself to process inputs and utilities (electricity, steam, oxygen) in a co-processing SAF example.
Worked comparison (p.32):
• Without flexible attribution of inputs: SAF GHG intensity = 68 g CO2e/MJ
• With flexible attribution of inputs: SAF GHG intensity = 30.25 g CO2e/MJ
Guardrail (Step 3, p.32): “You may not attribute more of an input than the amount... used in the co-process.” Low-carbon inputs are attributed first, up to their actual available quantity.
RSB-STD-01-010 v2.8, Annex V, pp.30–32.

## Slide 14
Backup 3
ISCC PLUS — the mass-balance foundation under Free Attribution
Chemical connectivity (§6.1, pp.17–18) — the precondition for any attribution, Free Attribution included: “Chemical link: the theoretical possibility of chemically converting the certified input(s) to the output(s)” plus “Process feasibility: availability of technical infrastructure.” Where both hold, “process outputs (products) can contain molecules or atoms of the certified input.”
General mass-balance rule (§6.2, p.18): “Under mass balance, the physical mixing of material with different sustainability characteristics and the mixing of certified and non-certified material is allowed, while ensuring that the sustainability characteristics remain assigned to physical batches of material on a bookkeeping basis.”
Four options under the Credit Method (Figure 6, p.26): Free Attribution, Fuel-Use Excluded Attribution, Proportional Attribution, Trace-the-Atom — each usable within the same §6.3 guardrails.
GHG/CI reporting sits outside this chapter entirely: ISCC PLUS 201 §2.4 (p.24) frames it as a “voluntary add-on” — “ISCC provides the option to adapt ISCC PLUS certificates to specific market requirements through voluntary add-ons.” Whether that add-on's calculation shifts with the attribution option chosen was not checked this review.
ISCC PLUS 203-2 Chain of Custody v1.1, §6.1–6.2, pp.17–18, 26; ISCC PLUS 201 System Basics v1.1, §2.4, p.24.